## Slide 1: User Datagram Protocol (UDP)

## Slide 2
Position of UDP in the layered architecture

## Slide 3: User datagram Protocol (UDP)
UDP is a transport protocol
  communication between processes
UDP uses IP to deliver datagrams to the right host
Connectionless
  No session is established.

## Slide 4: User datagram Protocol (UDP)
Does not guarantee delivery
  No sequence numbers
  No acknowledgements
  No flow control
  No error control
Reliability is the responsibility of the application. Uses Port numbers as endpoints to communicate

## Slide 5
User datagram format

## Slide 6
Why UDP ?
TCP is a complicated protocol involving :
  Flow control
  Exchange of acknowledgements
  etc.,
Hence for delay sensitive applications, TCP becomes inefficient
However TCP gives utmost importance for reliability ( but at the cost of efficiency )

## Slide 7
Why UDP ?
There are many applications which don’t demand reliability, but demand fast delivery
Typically audio / video streaming applications, where even loosing some bits doesn’t matter
In such cases UDP is preferred

## Slide 8
UDP is suitable for a process that requires simple request –response communication with little concern for flow and error control
It is not usually used for a process like FTP that needs to send bulk data

## Slide 9
UDP is suitable for a process with internal flow and error control mechanisms. For example Trivial File Transfer Protocol ( TFTP ) process includes flow and error control. It uses UDP

## Slide 10
UDP is used for management processes such as SNMP

## Slide 11
UDP is used for some route updating protocols such as RIP

## Slide 12
Applications of UDP
DNS –Domain Name Services
SNMP-Simple Network Management Protocol
TFTP – Trivial File Transfer Protocol
RTP – Real Time Protocol